Examining Ambiguities in the Automatic Packet Reporting System
Kenneth W. Finnegan, W6KWF
December 12, 2014

---
Overview
- Introduction to APRS and its capabilities
- Highlight many of the issues with APRS identified while working on this thesis
  - Bell 202 modulation
  - KISS modem interface
  - AX.25 addressing and routing
  - Tracker beaconing behaviors
- Questions and hopefully answers

---
What is APRS?
An ad-hoc message passing network
for short pieces of information

---
What is APRS?
- GPS Positions (Automatic Vehicle Location)
- Weather station readings
- Short (67 char) text messages
- Arbitrary system telemetry (i.e. battery voltage)
- Bulletins and announcements
- Remote command and control (i.e. turn light on)

---
The Three Types of APRS Nodes
- Trackers – Mobile APRS stations, often installed in cars, which feed most of the traffic into the network
- Digipeaters (Digis) – Digital repeaters which operate by storing and immediately forwarding packets on the APRS simplex channel
- Internet Gateways (I-gates) – Internet-connected APRS stations which feed local APRS traffic into the world-wide APRS-Internet System network

---
APRS Network Stack

---
Amateur Bell 202
- 1200bps modem developed in the early 1980s
- AT&T Bell 202 audio modems ordinarily used over telephone lines
- HDLC framing protocol as used under X.25
- Transmitted over VHF FM voice radios

---
Amateur Bell 202
(ASCII letter A - 0x41)

---
CRC-16-CCITT

---
Frame and AX.25 Format

---
Digipeater Aliases
WIDEn-N
 n – Hops originally requested
 N – Hops left to be consumed

---
(Actual) Digipeater Aliases
WIDEn-N
 n – All digipeaters if =1, else only high level
 N – Hops left to be consumed

---
Beaconing Algorithms
1. Fixed intervals
2. Time slots
3. Nice interval skipping
4. Fixed interval with dithering
5. SmartBeaconing

---
SmartBeaconing

---
Recommended Paths
- Mobile: “WIDE1-1,WIDE2-1”
- Fixed: Literal digi paths, or “WIDE2-1”
- Airborne: EMPTY
- “Proportional pathing”

---
RF Channel Capacity Model
1200bps channel bandwidth, but less than that in channel throughput

---
Questions?
Kenneth W. Finnegan, W6KWF
KennethFinnegan2007@gmail.com
http://blog.thelifeofkenneth.com/